## Slide 1: Data Sources and Conversion Feeding the GIS
Dr. Ahmad Bin Touq
abintouq@uaeu.ac.ae
http://faculty.uaeu.ac.ae/~abintouq
GEO 440: GIS for Urban & Regional Planning

## Slide 2: Data Sources and Conversion Feeding the GIS
Discussion here focuses more on projects than organization-wide implementation.
Like a teenager, a GIS can consume more than data you ever imagined!
Often, data collection is an end in itself. Almost invariably, it’s the costliest element of any project-- > 80%.

## Slide 3: Data Sources and Conversion Feeding the GIS.
Discussion here focuses more on projects than organization-wide implementation.
Like a teenager, a GIS can consume more than data you ever imagined!
Often, data collection is an end in itself. Almost invariably, it’s the costliest element of any project-- > 80%.

## Slide 4: Where do I get data? & What form is it in?
Where?
Secondary: existing data
  already published/available
  special tabulation/contract
Administrative records: data as by-product
  within your organization
  other organizations
Primary data: from scratch
  developed in-house (DIY)
  contracted out
(field work is always slow and expensive!)
What format?
  machine readable (digital)
  hardcopy (paper, maps)
Time
&
Cost
Increase
Applicability
&
suitability
generally
decrease.
Spatial data in digital form is the most valuable since this is generally the most expensive to obtain.

## Slide 5: Don’t forget to look in-house!
    collected by your organization as data
    by-product of normal agency operations
    acquired for some other project
    Don’t forget to look, especially if it’s a large organization. There may already be a GIS project in existense or about to be launched!

## Slide 6: Major GIS Data Sources
Maps
Drawings (sketch or engineering)
Aerial (or other) Photographs
Satellite Imagery
CAD data bases
Government & commercial spatial (GIS) data bases
Government & commercial attribute data bases
Paper records and documents

## Slide 7: Pre-processing and Conversion: almost invariably required!
Maps and Drawings
  digitizing, or
  scanning than raster to vector conversion
Aerial Photographs
  photogrammetry/photo interpretation to extract features
  digitizing or scanning to convert to digital
  rectification and DTM (digital terrain model) to create digital orthos
Satellite Imagery
  rectification and DTM to create digital orthos (if desired)
CAD Data Bases
  translator software (pre-existing or custom-written) needed to convert to required GIS format
GIS Data Bases
  conversion between proprietary standards (ARC/INFO, Intergraph, AutoCAD, etc.)
  Spatial Data Transfer Standard
Attribute Databases
  geocoding if micro data
  conversion between geographic units (e.g. zip codes and census tracts)
  conversion between different databases
Records and Documents
  OCR (optical character recognition) scanning
  keyboarding
  then, same as attribute data bases

## Slide 8: Data Conversions: general comments
Paper Maps to Digital
  generally the most complex & expensive
  automated extraction of layers problematic and error prone
    requires scanning then raster to vector conversion
  digitizing may be freehand with tablet, or “heads-up” on screen

## Slide 9: Data Conversions: general comments
Digital to Digital Conversions
  Safe Software’s Feature Manipulation Engine (FME) product provides translation between different vendor’s GIS formats
  spreadsheet software (Excel) is a powerful beginning point for converting to required database format (e.g. to .dbf for ArcView)
  specialized conversion packages for converting between different databases also available e.g. DBMS/Copy Plus, Data Junction
  efforts at standardization, which reduces need for conversions, have had limited success ‘cos of competitive pressures
    FGDC’s, Spatial Data Transfer Standard (SDTS), is a federal standard
    Open GIS Consortium, a vendor and user group, lobbies for standards and non-proprietary approaches to GIS database creation

## Slide 10: Data Conversion: hints on the process
NEVER CONVERT ON THE ORIGINAL FILE ALWAYS A COPY.
ALWAYS convert in an unrelated sub-directory
Document each new file that is made in the conversion process.
Archive the original files on a readily available media
Automate as many processes as possible
  Projections
  Many like files
  Replication of data for output
Record all your steps while converting data formats, in a journal or notebook. You WILL use that same conversion sometime in the future

## Slide 11: Data Sources: Table of Contents
Overview
Federal Data Sources: Spatial Data
Federal & Non-profit Data Sources: Attribute data
Private Sector Data Resources: Spatial and Attribute
Selected Sources in Detail
DIME
TIGER
USGS: Overview
  DEM detail
  DLG Detail
  DOQs and DLGs
Digital Chart of the World
NAVSTAR: gps
Remote Sensing
US Census Bureau Attribute Data
Primary Data Collection: Some Issues
As of Fall, 1999, single best web index to available data is:
http://cast.uark.edu/local/hunt/index.html

## Slide 12: Federal Data Sources: Spatial Data
Federal Data Agencies:
USGS (Geological Survey, National Mapping Div.--Interior)
  all kinds of mapping, not just geology!
NGS (National Geodetic Service-- Commerce, part of NOAA)
  geodetic surveying
[Ordnance Survey (in U.K.) combines both functions.]
Federal Mission Agencies
USDA (Agriculture)
  Resource Conservation Service (formerly Soil Conservation Service)
  US Forestry Service
DoD (Defense)
  National Imagery and Mapping Agency (NIMA)
    originally Defense Mapping Agency (DMA)
    US and world terrain mappings
  NAVSTAR: gps satellites
  US Army Corp. of Eng.: flood control
Interior
  US Fish and Wildlife: wetlands
  Bureau of Land Management
NASA (National Aeronautics and Space Administration
  LANDSAT satellites
Commerce
  Census Bureau: DIME & TIGER files
  NOAA (National Oceanic and Atmospheric Administration)
    AVHRR (Advanced Very High Resolution Radiometer) weather satellites

## Slide 13: Federal & Non-profit Data Sources: Attribute data
Federal Data Agencies
CB (Census Bureau-- Dept of Commerce)
  population and industry data from surveys
BEA (Bureau of Economic Analysis-- Dept. of Commerce)
  STAT-US: national accounts
Federal Mission Agencies
Most federal agencies now have a stat. dept
  Bureau of Labor Statistics
  National Center for Health Statistics
  National Center for Education Statistics
  National Center for Criminal Justice Statistics
  National Center for Transportation Statistics
  Interstate Commerce Commission
  Internal Revenue Service
Non-profit interest groups:
  Urban and Regional Information Systems Association (URISA)
  National League of Cities
  Population Reference Bureau
  Transportation Assoc. of America
Trade Associations:
  American Public Transit Assoc.
  see Encyclopedia of Associations
Trade Publications
  Progressive Grocer
  see Business Periodicals Index
University Research Centers
  University of Michigan, National Institute for Social Research

## Slide 14: Private Sector Data Resources
Spatial data
GIS software vendors
  e.g. ArcData Catalog
Satellite Data Sellers
  SPOT (French satellite)
  EOSAT (LANDSAT Thematic Mapper data)
Topological data (street networks and boundaries)
  Etak
  DeLorme
  Geographic Data Technology
Environmental
  Earthinfo
  Hydrosphere
Aerial Surveying/ Engineers/Consultants
  legions of them
  primary data
Attribute Data
Wide array of companies and services.
  pollsters and market surveyers
  remarketeers/updaters of federal gov. data (census data, TIGER files, etc..)
  data aggregators: collect admin. data from state and local gov. (e.g. building permits)
  gap fillers in government offerings
Larger providers include:
  Claritas/National Planning Data Corporation
  Equifax/National Decision Systems
  Blackburn/Urban Decision Systems
  SMI/Donnelly Marketing
Specialized providers include:
  Dun and Bradstreet (firms)
  TRW-REDI (property data)

## Slide 15: Vector Data Implementations: DIME file (Dual Independent Map Encoding)
introduced for the 1970 US Census and used again in 1980; replaced by TIGER in 1990
pioneering early example of topological structure
basic record was a line segment
flat file structure with all info in one record (Star and Estes misleading)
segments defined between every intersection for all linear features in landscape (streets, railroads, etc)
each segment record contained items such as:
  segment ID Segment type
  from node ID to node ID from node x,y to node x,y
  address range left address range right
  city left city right tract left tract right
  other left/right polygon ID info as needed e.g. county, block,
prepared only for metroplitan areas (278 files covering about 2% of nation)
some cities (very few) maintained and expanded (e.g add zoning) them after Census
inconsistent with Metroplitan Map Series paper maps published for each census
very compute intensive to process into continuous streets or polygons

## Slide 16: Vector Data Implementation: TIGER File (Topologically Integrated Geographic Encoding and Referencing file)
introduced for 1990 Census to eliminate inconsistencies between census products
cover entire country, and released by county
include hydrography, roads, railroads, etc.
uses relational data base model
data derived from 3 sources:
  scanned USGS 1:100,000 Map Series
  addresses ranges from DIME file, originally updated to 1986/7
  geographic area relationship files used by CB to process 1980 census
problems with TIGER
  accuracy limited by USGS base map and processing (100m horizontal)
  one time only; many segments missing.
  many local gov. records better
  data only: requires software to process.
First version was Tiger/1992
Latest is TIGER/Line 1998, issued July, 1999
comprises 6 record types (tables)
  basic data record (type 1): line segment records similar to DIME file
  shape coordinates (type 2): extra coords to define curved line segments
  area codes (type 3): block records giving higher order geog (tract, city, etc)
  feature name index (type 4): line segment records with code for alternative names (used when a segment has two or more charateristics (e.g both Main St and US 66)
  feature name list (type 5): names associated with codes n Type 4
  special addresses ranges (type 6): additional address ranges (e.g if zip code boundary splits a line segment
Minor differences exist in layout of various versions of TIGER which can lead to reading problems

## Slide 17: Vector/Raster Data Implementation: USGS (United States Geological Survey Digital Data)
Digital Elevation Model (DEM) data:
  Raster elevation data
  available at 30m, 2 arc second, and 3 arc second spacing (1 sec. of lat ~100ft)
Digital Line Graph Data (DLG) data
  digital representations of the cartographic line info. on main USGS map series.
  Vector planimetric data provided in full node/arc/polygon format
Land Use and Land Cover (LULC) data
  Land use and land cover data from 1:100,000 and 1:250,000 sheets
  Available in both raster format (4 hetare [10 acre] cells) and vector polygon format
Geographic Name Information System (GNIS) Data
  standardised place names and feature classification
Digital Orthoquads and Digital Raster Graphs
  raster data related to USGS 7.5 minute quads
Distibution of digital data by USGS began in the early 1980s. For details see:
USGS National Mapping Program USGS Digital Cartographic Data Standards, Washington, D.C.: Geological Survey Circular 895A thru G, 1983.

## Slide 18: USGS: DEM Data Detail (Digital Elevation Model)
Raster elevation data.
7.5 minute, 1:24,000 USGS quads (15 minutes in Alaska)
  elevations at 30 meter spacing
  UTM coords, NAD27 datum
  accuarcy: <15m RMSE (some <7) (horizontal: 15m)
30 minute, 1:100,000 USGS topo sheet
  2 arc second spacing
  NAD27 datum
  accuracy: 5-25m--1/2 map contour int. (horizontal: 50m)
1 by 2 degree, 1:250,000 USGS sheets
  from Defense Mapping Agency (DMA)
  3 arc second spacing
  WGS72 datum
  variable: 30-75m (horizontal: 100m)
Each file has three records:
  Record A: descriptive information
  Record B: elevation data
  Record C: accuracy statistics
Files classified into one of three levels depending on editing, etc
  Level 1: raw elevation data; only ‘gross blunders’ corrected.
  Level 2: data edited and smoothed for consistency.
  Level 3: data modified for consistency with planimetric data such as hydrography and trans.

## Slide 19: USGS DLG Data Detail (Digital Line Graph)
Three products:
Large Scale (ls) -- generally 1:24,000
  7.5 minutes per file
Medium Scale (ms) -- 1:100,000
  30x30 minute files (half a map sheet)
Small Scale (ss) --1:2,000,000
  21 files for nation (one CD-ROM)
Three formats:
Standard (no longer available)
  internal cartesian coords (saves storage)
  limited topological info;
Optional (DLG-3) (use for GIS):
  UTM metric (Albers Equal Area Polyconic for small scale)
  full topological info
Graphic (small scale only)
  GS-CAM compatible; no topological info.
  OK for display
Coverages (up to 9)
  Hydrography: all flowing and standing water, and wetlands
  Hypsography: contours and elevation
  Transportation: roads, trails, railroads, pipelines, transmission lines
  Boundaries: political & administrative
  Public Land Survey System (PLSS): township, range, section (not ss)
  Vegetative surfaces (ls only)
  Non-veg surfaces (e.g. sand) (ls)
  survey control and markers (ls)
  manmade features (e.g. buildings)(ls)
Horizontal Accuracy:
  large scale (7.5min.): 12-50m
  medium (1:100,000): 50m
  small : ??

## Slide 20: USGS New Products DOQs and DRGs
Digital Ortho Quads (still in progress--depends on state/local cooperation)
Digital image of an aerial photo in which displacement caused by camera lens, airplane’s position, and the terrain have been removed-- image characteristics of a photo and geometric properties of a map.
1:12,000 scale; UTM coords, NAD83 datum
1 meter resolution; 33 feet (10m) positional accuracy (national map stand.)
associated DEM (digital elevation model) 7m vertical accuracy
quarter quadrangle coverage: 3.75 by 3.75 minutes
use as base for topo and planimetric maps (if accuracy is sufficient)
Digital Raster Graphics
Scanned image of USGS topo map, recast in some cases to UTM.
1:24,000/7.5 quads current; 1:100,000 & 1:250,000 future
250dpi; 8-bit color; TIFF file; 64 per CD-ROM
use as backdrop/validation for other digital data

## Slide 21: Digital Chart of the World
spatial data base of the world.; 1st released cerca 1992
1:1 million target mapping scale
US DoD project in coop. with Canada, Australia, and UK
1.7GB of data on 4 CD-ROMs (North America, Europe/Northern Asia, South America/Africa/Antarctica, SouthernAsia/Australia). $200 cost
derived from DMA's 1:1 million scale Operational Navigational Chart (ONC) base maps
in Vector Product Format (VPF), but also available in most GIS vendor formats, and ASCII
The VPFVIEW 1.1 freeware for DOS and SUN OS available to view VPF
World Geodetic System 84 datum
Airports, boundaries, coastal, contours, elevation, geographic names, international boundaries, land cover, ports, railroads, roads, surface and manmade features, topography, transmission lines, waterway
1,000 ft contours with 250ft supplements
17 layers with 31 feature classes
* Aeronautical Information
* Cultural
* Landmarks
* Data Quality
* Drainage
* Supplemental Drainage
* Utilities
* Vegetation
* Supplemental Hypsography
* Land Cover
* Ocean Features
* Physiography
* Political
* Populated Places
* Railroads
* Roads
* Transportation Structures
worldwide index with 100,000 place name

## Slide 22: NAVSTAR Global Positioning System (gps)
NAVSTAR Satellite Program
25 (NAVigation Satellite Time and Ranging) satellites in 11,00 mile orbit provide 24 hour coverage worldwide
first launched 1978; full system operational December 1993.
gps receiver computes locations/elevations via signals from 3-5 simultaneously visible satellites
Selective Availability (SA) security system
  100m accuracy with single receiver, if active
  10-15m accuracy if inactive
  mutiple receivers &/or correction info. (from multiple sources) counteract SA
  to be turned off in year 2000
USCG broadcasts correction signal!
Russia’s 21-satellite GLONASS (Global Navigation Satellite System) also available.
Types of Ground Collection
  kinematic:
  high accuracy engineering (within cms);
  two receivers (base station and rover
  must lock-on to satellites
  equipment $18-35K per station
  differential
  surveying accuarcy (1-5m)
  no lock required
  equipment $1,500-$15,000 per receiver
  correct for SA and other errors via
    real time correction signal
    post process with data from Internet
  connect to laptop PC for direct data input and entry of attribute info.
  use to collect ground control for digital orthos, or for point/line data collection (manholes, roads, etc)
  cost now $10-25 per point ( $100 a few years ago)
  autonomous (navigational/recreational)
  100m accuracy generally (10m without SA)
  single, hand-held unit
  $150-$1,500 per unit

## Slide 23
Longitude (secs. from 96° 43’)
Latitude (secs. from N 32° 56’)
plots of positions collected by Garmin 38 GPS receiver at same location on three successive occasions
approximately 200 points per plot.
one point collected per 2 seconds.
1 second of latitude approx. 30m
1 second of longitude approx. 25m
(location: 524 Highland Blvd, Richardson, TX)
(satellite
view
restricted)

## Slide 24
1 second of latitude is approx. 30 meters.
1 second of longitude (@32N) is 25 meters.
* satellite view restricted

## Slide 25: Factors Affecting GPS Accuracy
ionosphere
  worst in evening at low altitudes (but ephemerous best there)
troposhere
  especially water vapor which slows signal
multipath
  reflected signals from buildings, cliffs, etc
ephemerous
  position and number of satellites in sky
  4 required for 3D (horiz. and vertical), 3 for 2D (no elevation)
  ideallly, 3 every 120° horizon. with 20° elev., 1 directly above
blockage (of satellite signal)
  by foliage, buildings, cliffs, etc.

## Slide 26: GPS Receiver Characteristics
Irrespective of cost ($150 to $50,000) all have same accuracy in autonomous mode!
processing speed & channel capacity (# of satellite data streams simultaneously processed)
storage capability: internal & PCM/CIA cards
codes it can process (L1, L2; code, carrier phase, etc.)
antenna type and remote connection support
interface capabilities
  RTCM: standard for input of differential correction signal
  NMEA (National Marine Electronics Association):positions for real-time interface to instruments (also to PC software e.g. for location on a map)
  RINEX (receiver independent exchange): output of raw satellite data for post processing
  other proprietary: for waypoints, routes, position data, etc. upload/ download
specialized user support features (hiking, marine nav., surveying, civil eng., etc.)

## Slide 27: Remote Sensing
remote sensing: info. via systems not in direct contact with objects of interest:
  via cameras recording on film, which may then be scanned (primarily aerial photos)
  via sensors, which directly output digital data (primarily satellites, but also planes)
image processing: manipulating data derived via remote sensing
photographic film types:
  monochrome (black and white)
  natural color
  infra-red (insensitive to blue, but goes past visible red; good for geology, veg. , heat)
types of sensors
  passive (most common): record natural electromagnetic energy emissions from surface
  active (radar): record reflected value of a transmitted signal (e.g. Canada’s RADARSAT, NASA’s SIR-C/X-SAR)
    penetrate clouds; also, some ground penetration possible.
passive sensors: typically store one byte of info (256 values) per spectral band (a selected wavelength interval in the electromagnetic spectrum);
  panchromatic: single band recorded (e.g. SPOT Panchromatic)
  multi-spectral: multiple bands recorded (e.g. LANDSAT MMS-4, TM-6)
  hyperspectral: hundreds of bands (TRW’s proposed Lewis satellite has 384)
spectral signature: the set of values for each band typifying a particular phenomena (e.g. blighted corn, concrete highway) to allow unique identification

## Slide 28: Current Satellites
Source: Keating, BLM Tech. Note # 389, 1993

## Slide 29: Next-Generation Satellites (selected) expected to generate at least 750 GB of data per day--”Beam me down, Scotty!”
Source: Carlson and Patel, GIS World, March 1997
ASPRS Land Satellite Information for the Next Decade, conference proceedings, Sept 1995
resolution in meters; revisits in days
Resolution of new satellites makes urban mangement applications possible.

## Slide 30: Some Notes on New Satellites (early 1997)
Satellites vary by: orbit, altitude, revist variability (steering) capability, width of swath, image size, stereo capability, wavelengths collected, other sensors, etc.
EarthWatch: WorldView Imaging Corp and Ball Aerospace with Hitachi (Japan), Nuova Telespazio (Italy),MacDonald Dettwiler (Canada), CTA Space Systems (Rockville, MD), Datron (Escondido, CA)
Space Imaging/EOSAT: Lockheed Martin, Raytheon/E-Systems,Mitsubishi, Kodak. Purchase of EOSAT (Earth Observation Satellite Company) in 11/96 and formation of a Mapping Alliance Program with 10 big-time aerial mapping companies [e.g Woolpert (Dayton), Analytical Surveys, Inc (Colorado Springs)], makes them a powerhouse for data.
TRW: part of NASA’s Small Spacecraft Technology Initiative, with satellite built by CTA
the Global Change research project’s Earth Observation System (EOS), which includes NASA’s Mission to Planet Earth, includes a wide variety of monitors & sensors on multiple satellites from different countries through 2008
Countries with existing/planned satellites include: Argentine, Brazil, Canada, France, Germany, India, Israel, Japan, Korea (South), Ukraine, US.

## Slide 31: The Relative Cost of Different Options (as of 1993)
Satellite Remote Sensing
Maps and Existing Digital data
Photogrametry
Global Positioning System
Survey
1cm
1m
30m
1cent
$100
$1,000
least accurate
least
expensive
Source: Keating, BLM Tech. Note # 389, 1993

## Slide 32: U.S. Census Bureau: Attribute Data (see: Census Catalog and Guide published annually)
Census of Population and Housing
  10 year cycle (1990)
  two main tabulations
    Full count (STF1 & 2)
      geog. detail
      down to block
    Sample (STF3 & 4)
      20% stratified sample
      ‘long form’
      attribute detail
Economic Census
  5 year cycle (1993)
  agriculture, retail, manufacturing, service, transportation, government, construction
Data Collection Methodologies
Census
  mandatory, entire population
  regular but infrequent, as benchmark
Update surveys
  not mandatory, update censuses
  limited geog detail, usually annual (some weekly)
Special Surveys
  not mandatory; cover data not in census
  often on contract with other agency (e.g National Health Survey)
Non-Survey
  admin records from other agencies
  update census (e.g. Current Poplation Reports)
  provide additional info (e.g. County Business Patterns)

## Slide 33: Aggregation Issues in Attribute Data
Disaggregate (micro) data
individuals or individual entities
  persons, households, firms,
  parcels, housing units, establishments
  trees, poles, wells
geocoding required
confidentiality/disclosure a critical issue
suppresion may be imposed on aggregate data
Aggregate data
groups of individuals or entities
  by geographic area--block, tract
  by time: rainfall/sales by day, month, year
  by characteristic: age group, race, species
polygons required for mapping
Cross-sectional: different spatial units at one point in time
Longitudinal: one spatial unit at different points in time
Dynamic: continuously produced over time and space (some satellites; CORS program)

## Slide 34: Samples, Populations and Spatial Patterns Some Issues for Primary Data Collection
Population: --all instances of a phenomena
Sample: subset of population
random: each pop. member has equal chance of being chosen
systematic: members chosen based on repetitive rule (every 10th; every 4 feet)
stratified:; sampling conducted within groups to ensure representation
Especially tricky for spatial data!
random
Spatial sampling methods
  point: collect info at one spot
  transect: along a line
  quadrat: within a square
clustered
dispersed
Probability of one point being close to another
equal
high
low

## Slide 35: Summary of Data Collection Issues Suitability/Appropriateness for the Task
horizontal (and vertical) accuracy:
  33 feet USGS DOQ, versus 3 feet for urban needs
documentation
  often bad for administrative records
currency and frequency of update
  is date and/or update cycle appropriate?
completeness
  is undercount/omission a serious problem?
  e.g. most ‘lists’ miss the poor (census undercounts); TIGER file once per decade
aggregation and sampling
  are they appropriate?
cost -- highly associated with accuracy
  is cost within budget?
  is benefit greater than cost?